Name : Rehan Shakoor
Submission Date : 23/10/2024

Project Report
Car Black Box

Project Description :

Project is to make a fully functional black box for a car. Black box is used to store events which happens with the vehical, like gear change, collision, speed etc.

These records are important for accident cause analysis and to check traffic rules are followed properly or not.

Microcontroller used :

In this project PIC16F877A (8-bit), microcontroller is used. MPLAB IDE is used to do all register level coding using C language.

Black Box Features :

1) Operational Mode :

In this mode, we can see time, event and speed of vehical.
Time is read from external RTC connect to controller via I2C communication protocol.
Speed is read from potentiometer, which is connect to ADC input pin.
Switch interrupts are used to change gear and to denote collision.

2) Event Capture :

When some gear is changed or collision happens, then current time, gear value and speed is stored in external EEPROM. This EEPROM is conencted via I2C protocol.

3) Login screen :

User have to enter a password, to login into the device.

4) Menu screen :

In menu we can, view logs which are stored in external EEPROM.
We can set RTC time.
We can see all logs stored in EEPROM on serial terminal (UART).
We can clear all logs.